## Slide 1: Micron Project
PFAS 1,2,4 Triazole BOD COD TOC
21 Sep 2023
Song Heng, Chen Yang & Angela

## Slide 2: Background & Objective
Wastewater samples collected from Singapore Micron site
Analysis parameters include TOC, COD, BOD, PFAS and 1,2,4 triazoles
This analysis is as a reference to the Micron Boise Opal and 1D1 WW project

## Slide 3: Collected Samples
Wastewater collecting Time & Date: 20 Sep 2023, 15:30
Solid sample collectime Time & Date: 19 Sep 2023, 17:00
No. | Sample Label | Testing Paramters | Note
1 | HFW Filtrate Water | PFAS, 1,2,4 Triazole, BOD, COD, TOC | Wastewater Sample
2 | HFW EQ Tank Outlet | PFAS, 1,2,4 Triazole, BOD, COD, TOC | Wastewater Sample
3 | LSR2 Incoming | PFAS, 1,2,4 Triazole, BOD, COD, TOC | Wastewater Sample
4 | LSR2 ROi Permeate | PFAS, 1,2,4 Triazole, BOD, COD, TOC | Wastewater Sample
5 | LSR2 ROi Reject | PFAS, 1,2,4 Triazole, BOD, COD, TOC | Wastewater Sample
6 | Filter Press | PFAS, 1,2,4 Triazole | Solid Sample

## Slide 4: Micron SG Site water
Concentration (mg/L) | HFW Filtrate water | HFW EQ Tank water | LSR2 Incoming | LSR2 Roi Permeate | LSR2 Roi Reject | Filtrate Press (Solid)
Tested COD (mg/L) | 99 | 235 | 10 | 7 | 6 | N.A.
Tested TOC (mg/L) | 15.47 | 21.94 | 1.59 | 0.36 | 2.17 | N.A.
Tested COD/TOC | 6.4 | 10.7 | 6.3 | 19.2 | 2.8 | N.A.
Tested BOD (mg/L) | 2.57 | 9.5 | 11.8 | N.D. | N.D. | N.A.
1,2,4 Triazole (µg/L or µg/g for solid) | 4.05 | 6.48 | 22.22 | 18.88 | 21.01 | 4.88
Total PFAS (µg/L or µg/g for solid) | 37.87 | 39.2 | 47.57 | 0.035 | 0.73 | 112.7