## Slide 1: Micron Project
TMAH IPA PFAS 1,2,4 Triazole BOD COD TOC
19 Sep 2023
Song Heng, Chen Yang & Angela

## Slide 2: Background & Objective
To find out the COD/TOC ratio and BOD for various combination of TMAH, IPA mixture solutions
ThOD/Theoretical TOC ratio for both TMAH and IPA are 4
TMAH skips HACH COD testing, BOD also super low

## Slide 3: Experiments on TMAH
Tap water, Tetramethylammonium hydroxide pentahydrate
(CH3)4N(OH) · 5H2O
(CH3)4N(OH) · 5H2O (mg/L) | 10 | 50 | 100 | 150 | 300 | 3000
TMAH - (CH3)4N(OH) (mg/L) | 5.03 | 25.15 | 50.3 | 75.45 | 150.9 | 1509
ThOD (mg/L) | 10.6 | 53 | 105.9 | 158.9 | 317.8 | 3178.4
Theoretical TOC (mg/L) | 2.65 | 13.24 | 26.49 | 39.73 | 79.46 | 794.61
COD from Literature (mg/L) | 0 | 0 | 0 | 0 | 0 | 0
Estimated COD/TOC | 0 | 0 | 0 | 0 | 0 | 0
BOD from Literature (mg/L) | 0 | 0 | 0 | 0 | 0 | 0.24
Tested COD (mg/L) | U.D | U.D | U.D | U.D | U.D | U.D
Tested TOC (mg/L) | 2.785 | 13.23 | 25.42 | 37 | 80.05 | 760.4
Tested COD/TOC | N.A | N.A | N.A | N.A | N.A | N.A
Tested BOD5 (mg/L) | N.D. | N.D. | N.D. | N.D. | N.D. | N.D.

## Slide 4: Experiments on TMAH
Chart: TMAH Concentration (mg/L)
| 5.03 | 25.15 | 50.3 | 75.45 | 150.9 | 1509
TOC | 2.785 | 13.23 | 25.42 | 37 | 80.05 | 760.4

## Slide 5: Experiments on IPA
Tap water, chemistry grade chemicals
IPA (mg/L) | 100 | 500 | 1000 | 2000 | 3000 | 5000
ThOD (mg/L) | 239.6 | 1198 | 2396 | 4792 | 7188 | 11980
Theoretical TOC (mg/L) | 59.9 | 299.5 | 599 | 1198 | 1797 | 2995
COD from Literature (mg/L) | 223 | 1115 | 2230 | 4460 | 6690 | 11150
Estimated COD/TOC | 3.72 | 3.72 | 3.72 | 3.72 | 3.72 | 3.72
BOD from Literature (mg/L) | 119 | 595 | 1190 | 2380 | 3570 | 5950
Tested COD (mg/L) | 182 | 776 | 2400 | 5570 | 8530 | 12150
Tested TOC (mg/L) | 46.02 | 179.75 | 428.8 | 1005 | 1585 | 2828
Tested COD/TOC | 3.95 | 4.32 | 5.60 | 5.54 | 5.38 | 4.3
Tested BOD5 (mg/L) | 5.4 | 97.1 | 44.9 | 125 | 55.4 | 171

## Slide 6: Experiments on IPA
Chart: TMAH Concentration (mg/L)
| 100 | 500 | 1000 | 2000 | 3000 | 5000
TOC | 46.02 | 179.75 | 428.8 | 1005 | 1585 | 2828
Chart: TMAH Concentration (mg/L)
| 100 | 500 | 1000 | 2000 | 3000 | 5000
COD | 182 | 776 | 2400 | 5570 | 8530 | 12150

## Slide 7: Experiments on TMAH & IPA Mixture Solutions
Concentration (mg/L) | TMAH 50 IPA 50 | TMAH 50 IPA 100 | TMAH 150 IPA 100 | TMAH 150 IPA 1000
ThOD (mg/L) | 225.1 | 344.9 | 555.5 | 2712
Theoretical TOC (mg/L) | 56.3 | 86.2 | 138.9 | 678
COD from Literature (mg/L) | 111.5 | 223 | 223 | 2230
Estimated COD/TOC | 1.98 | 2.59 | 1.61 | 3.29
BOD from Literature (mg/L) | 59.5 | 119 | 119 | 1190
Tested COD (mg/L) | 141 | 251 | 194 | 1740
Tested TOC (mg/L) | 58.12 | 82.98 | 120.5 | 639.9
Tested COD/TOC | 2.43 | 3.02 | 1.61 | 2.3
Tested BOD5 (mg/L) | N.D. | N.D. | 4.11 | 253