## Slide 1: Micron ID1
Keng Wai Ren
05 Dec 2024
Rev 1

## Slide 2: Objective
To evaluate the water chemistry for CFRO brine to ATFD
  Mix TMAH and Aquatar into CFRO brine and send for ATFD
  200,000 mg/l NaCl, 1000 mg/l TMAH, 50 mg/l Aquatar
  Test distillate for TMAH and Aquatar

## Slide 3: Test Methodology
Prepare Synthetic Feed – 1L
  Synthetic feed was prepared with DI water and NaCl.
  TMAH and Aquatar were added into the solution.
Perform water analysis
  Analyse synthetic feed with TOC/TN.
  Feed was split into two jars. Distillation with and without vacuum.
  Distillates were collected and analysed for COD, TOC and TN
Determine Crystals Structure
  Salt cake formed was collected.

## Slide 4: Water Analysis – For MLD Application
Samples | COD | TOC | TN
Feed | * | 514.4 | 162.2
Distillate 2 | 1136 | 242.4 | 1
Distillate 3 | 84 | 23.16 | 0.81
Distillate 4 | 8 | 1.731 | 0.248
Distillate combined | 18 | 17.94 | 4.38
Conc | * | 1287.2 | 458.8
Distillation with vacuum
*Not measured due to high chloride interference

## Slide 5: Water Analysis – for ZLD Application
Samples | COD | TOC | TN
Feed | * | 514.4 | 162.2
Distillate initial | 10 | 5.191 | 0.21
Distillate final | 85 | 61 | 17
Distillation
*Not measured due to high chloride interference
Final operating temperature approximately 140C.

## Slide 6: Salt Cake Collected